## Slide 1: Gamma-400 “new” calorimeter status
Oscar Adriani
INFN and University of Florence
Trieste, May 5th, 2013

## Slide 2: Starting point
The starting point is the presentation at the Moscow meeting in February
No change in the proposed structure
New results from:
  Simulation (Rejection factor)
  Test beam data analysis
Meanwhile we have provided to Russian colleagues the description of the pre-prototype, that will be sent in Russia
The electrical interface document is under preparation by Trieste peoples
The calorimeter proposal should be updated according to the discussion under way in Russia:
  increase the weight of the payload
  Increase the top surface of the calorimeter to increase the gamma acceptance
Scaling of the calorimeter is feasible and should be studied

## Slide 3: The proposed configuration: CsI(Tl) ~ 1680 kg
 | Cubes
NNN | 202020
L of small cube (cm) | 3.6*
Crystal volume (cm3) | 46.7
Gap (cm) | 0.3
Mass (Kg) | 1683
N.Crystals | 8000
Size (cm3) | 78.078.078.0
Depth (R.L.) “ (I.L.) | 393939 1.81.81.8
Planar GF (m2sr) ** | 1.91
(* one Moliere radius)
(** GF for only one face)
Very deep!!!!

## Slide 4: The readout sensors
Minimum 2 Photo Diodes are necessary to cover the whole huge dynamic range
1 MIP107 MIPS, since Emax in one crystal ~ 0.1 Etot
Large Area Excelitas VTH2090 9.2 x 9.2 mm2 for small signals  Inserted in the simulation!
Small area 0.5 x 0.5 mm2 for large signals
Two independent readout channels will be used
Details later on!

## Slide 5: Mechanical idea

## Slide 6: Simulation
FLUKA based simulation
Planar generation surface on one of the 5 faces
Results valid also for the other faces!
Carbon fiber in between crystals (3 mm gaps)
Large photodiode is inserted on the crystal in the simulation
  We take into account also the energy release in the Photodiode itself!
  Results are valid for every face since scintillation light is isotropically emitted
Electrons: 100 GeV – 1 TeV range
Protons: 100 GeV – 100 TeV range
~ 100 – 10.000 events for each energy
No mis-calibration effects are included in the simulation
Light collection efficiency and PD quantum efficiency are included in the simulation
For the moment we have very low statistics for high energy particles (huge computing time is necessary….)

## Slide 7: Electrons
Selection efficiency:
ε ~ 36%
GFeff ~ 3.4 m2sr
Electrons 100 – 1000 GeV
(Measured Energy – Real Energy) / Real Energy
Crystals only
Crystals + photodiodes
Non-gaussian tails due to leakages and to energy losses in carbon fiber material
RMS~2%
Ionization effect on PD: 1.7%

## Slide 8: Protons
Energy resolution
Selection efficiencies:
ε0.1-1TeV ~ 35%
ε1TeV ~ 41%
ε10TeV ~ 47%
GFeff0.1-1TeV ~ 3.3 m2sr
GFeff1TeV ~ 3.9 m2sr
GFeff10TeV ~ 4.5 m2sr
100 TeV
40%
(Measured Energy – Real Energy) / Real Energy
10 TeV
39%
(Measured Energy – Real Energy) / Real Energy
100 – 1000 GeV
32%
(Measured Energy – Real Energy) / Real Energy
1 TeV
35%
(Measured Energy – Real Energy) / Real Energy

## Slide 9
Proton rejection factor
Montecarlo study of proton contamination
using CALORIMETER INFORMATIONS ONLY
PARTICLES propagation & detector response simulated with FLUKA
Geometrical cuts for shower containment
Cuts based on longitudinal and lateral development
LatRMS4
protons
electrons
LONGITUDINAL
LATERAL
155.000 protons simulated at 1 TeV : only 1 survive the cuts
The corresponding electron efficiency is 37% and almost constant with energy above 500gev
Mc study of energy dependence of selection efficiency and calo energy distribution of misreconstructed events
10TeV
1TeV
l1

## Slide 10
E(GeV)
E3dN/dE(GeV2 ,s-1 )
Protons in acceptance(9,55m2sr)/dE
Electrons in acceptance(9,55m2sr)/dE
vela
Electrons detected/dEcal
Protons detected as electrons /dEcal
Contamination :
0,5% at 1TeV
2% at 4 TeV
An upper limit
90% CL is obtained
using a factor X 3,89
Proton rejection factor
= = 0,5 x 106
X Electron Eff. ~ 2 x 105

## Slide 11: The prototypes and the test beams
Two prototypes have been built at INFN Florence, with the help of INFN Trieste, INFN Pisa and University of Siena.
A small, so called “pre-prototype”, made of 4 layers with 3 crystals each
  12 CsI(Tl) crystals, 2.5x2.5x2.5 cm3
A bigger, properly called “prototype”, made of 14 layers with 9 crystals each
  126 CsI(Tl) crystals, 3.6x3.6x3.6 cm3
Both devices have been tested at CERN SPS (pre-prototype in October 2012 and prototype in January-February 2013)

## Slide 12: The prototype

## Slide 13: The prototype

## Slide 14: Noise
CN evaluated with disconnected channels and 4-sigma cut
WITH and WITHOUT CN subtraction

## Slide 15: Noise studies
The noise of the 16 CASIS channels is correlated, but not in a clear way (for example the correlation coefficient for the disconnected channels is not very high)
When we have a shower it is not so clear how to compute the CMN
  Disconnected channels do not give a good estimate
  It is not so clear how to identify the signals without signals (if there are….)
Result  The CMN subtraction does not give clear advantages, mainly if showers are present…

## Slide 17: Hit definition
S’=ADC-PED-CN
S=ADC-PED
Hit defined by 4-sigma cut on S’

## Slide 18
First layer used to select Z=1 and Z=2 nuclei.
Z=1
Z=2
30GV

## Slide 19
Layer with MAX hit
Shower START  First layer with a hit > 15 MIP
30GV
Z=1

## Slide 20
Layer with MAX hit
Shower START  First layer with a hit > 15 MIP
30GV
Z=2

## Slide 21
Z=2
Z=1
30GV
Total energy deposit VS shower-starting layer
Maximal containment when starting-layer == 2

## Slide 22
Z=2
Z=1
30GV
Average longitudinal profile
(Starting layer == 2)

## Slide 23: Energy resolution
30 GV
Starting-layer ==2
Z=2
Z=1
58% (fit)
37% (fit)
Superposition principle:

## Slide 24: Calibation of the crystals
Before calibration
After calibration

## Slide 25: Response uniformity of the crystals
~14% Uniformity

## Slide 26: A strange effect….
To be checked!!!
Particles hitting the PD?
Effect seen by Ferm????

## Slide 27: A glance at prototype's TB data
H: Z=1 <ADC>=330
He: Z=2 <ADC>=1300
Li: Z=3 <ADC>=3000
Be: Z=4 <ADC>=5300
B: Z=5 <ADC>=8250
C: Z=6 <ADC>=12000
N Z=7 <ADC>=16000
He
Li
Be
B
C
N
Please remind that this is a calorimeter!!!!
Not a Z measuring device!!!!

## Slide 28: Energy deposit for various nuclei
Charge is selected with the placed-in-front tracking system
Good Linearity even with the large area PD!
Preliminary
Courtesy of Pi-Si group

## Slide 29
Courtesy of Pi-Si group

## Slide 30: How to improve the calorimeter performances?
We could try to see the Cherenkov light produced in the crystals by the electromagnetic component of the shower
  Improvement of the e/p rejection factor
  Improvement of the hadronic energy resolution (DREAM project)
Problem: different response to electromagnetic and hadronic particles (e/h>1)
Effect: worsening of energy resolution
Solution: try to compensate the hadronic response to make it equal to electromagnetic one
  ‘Software compensation’ developed in the last few years
  Hardware compensation (~late 1980)

## Slide 31: Some ideas for the Cherenkov light
Use of SiPM to detect Cherenkov light
  Discrimination btw Fast Cherenkov light and Slow Scintillation light possible with dedicated fast sampling electronics
  Use of SiPM highly sensitive in the UV region
Use of ‘UV transmitting’ filters on the SiPM face
  to block the largely dominant scintillation light
Possible use of ≥3 SiPM for each crystal on orthogonal faces
  to have a good uniformity in the response for particles hitting the different calorimeter’s faces
Dedicated test beam at INFN-Frascati in October
  700 MeV electron beams
  Few crystals equipped with UV-transmitting filters and SiPM

## Slide 32: Which Calorimeter can we put in Gamma-400?
Basic idea: remove CC1, use only CC2
Few layers of silicon in between the first few layers of crystals to obtain the desired angular resolution are possible
Remind:
  Basic CCUBE:
    0.78m x 0.78m x 0.78m=0.475 m3, 8000 crystals, 1683 kg
  Starting russian design (from Sergey design):
    9400 crystals + 2 X0 CC1=9400+’784 equivalent crystals’=10180 crystals, 2140 kg
Possible proposal:
  A Dream….: 1m x 1m x 0.8 m: 13.300 crystals, 2790 kg
  Still a Dream…: 1m x 1m x 0.7 m: 11.600 crystals, 2440 kg
  A Realistic Dream: 1m x 1m x 0.65 m: 10.800 crystals, 2260 kg
  A very good det.: 1m x 1m x 0.6 m: 9.975 crystals, 2090 kg

## Slide 33: Conclusion
An homogeneous, isotropic calorimeter looks to be an optimal tool for Gamma-400-N
The status of the project is quite advanced:
  Simulation
  Prototypes
  Test beams
Next steps:
  R&D on the Cherenkov light during 2013 and 2014
  Possibly enlarge the prototype’s dimensions
  Low energy electron test beam in INFN Frascati in autumn 2013
  Test at Serpukhov with high energy protons and electrons in 2014
  R&D for the Calibration system of every crystal is certainly necessary!
    Possible synergy and help from the russian colleagues for this item?

## Slide 34: Backup

## Slide 35: Shower starting point resolution
<ΔX> = 1.15 cm

## Slide 36
Shower Length (cm)
Signal / Energy
Proton 1 TeV

## Slide 37
Shower Length (cm)
Signal / Energy
Proton 10 TeV

## Slide 38
Calibration curves
Shower Length (cm)
100 – 1000 GeV
1 TeV
10 TeV
Signal / Energy

## Slide 39
Counts estimation, electrons
G400 configuration: CsI(Tl), 20x20x20 crystals
Size: 78.0x78.0x78.0 cm3 – gap 0.3 cm
Taking into account: geometrical factor and exp. duration +
selection efficiency 80%
Experiment | Duration | Planar GF (m2 sr) | Calo s(E)/E | Calo depth | e/p rejection factor | E > 0.5 TeV | E > 1 TeV | E > 2 TeV | E > 4 TeV
CALET | 5 y | 0,12 | ~2% | 30 X0 | 105 | 3193 | 611 | 95 | 10
AMS02 | 10 y | 0,5** | ~2% | 16 X0 | 103 ** | 26606 | 5091 | 794 | 84
ATIC | 30 d | 0,25 | ~2% | 18 X0 | 104 | 109 | 21 | 3 | 0
FERMI | 10 y | 1,6@300 GeV * 0,6@800 GeV * | ~15% | 8,6 X0 | 104 | 59864 | 2545 | 0 | 0
G400 | 10 y | 8,5 | ~0,9% | 39 X0 | 106 | 452303 | 86540 | 13502 | 1436
* efficiencies included
** calorimeter standalone

## Slide 40
Experiment | Duration | Planar GF (m2 sr) | e sel | Calo s(E)/E | Calo depth | E > 0.1 PeV |  | E > 0.5 PeV |  | E > 1 PeV |  | E > 2 PeV |  | E > 4 PeV | 
 |  |  | e conv |  |  | p | He | p | He | p | He | p | He | p | He
CALET | 5 y | 0,12 | 0,8 | ~40% | 30 X0 1,3 l0 | 146 | 138 | 9 | 10 | 2 | 3 | 1 | 1 | 0 | 0
 |  |  | 0,5 |  |  |  |  |  |  |  |  |  |  |  | 
CREAM | 180 d | 0,43 | 0,8 | ~45% | 20 X0 1,2 l0 | 41 | 39 | 3 | 3 | 1 | 1 | 0 | 0 | 0 | 0
 |  |  | 0,4 CT* |  |  |  |  |  |  |  |  |  |  |  | 
ATIC | 30 d | 0,25 | 0,8 | ~37% | 18 X0 1,6 l0 | 5 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  |  | 0,5 CT* |  |  |  |  |  |  |  |  |  |  |  | 
G400 | 10 y | 8,5 | 0,8 | ~17% | 39 X0 1,8 l0 | 16521 | 15624 | 979 | 1083 | 261 | 326 | 60 | 92 | 10 | 21
 |  |  | 0,4 |  |  |  |  |  |  |  |  |  |  |  | 
~ knee
Counts estimation, protons and helium nuclei
* carbon target
Polygonato model
G400 configuration: CsI(Tl), 20x20x20 crystals
Size: 78.0x78.0x78.0 cm3 – gap 0.3 cm
Taking into account: geometrical factor and exp. duration + selection
efficiency 80%

## Slide 41
Total silicon signals / Total crystal signals
Electrons

## Slide 42
Emax ~ 0.1× Etot

## Slide 43
ΔE = 17%
Energy resolution

## Slide 44: Electrons
Very simple geometrical cuts:
The track should point to a fiducial surface (two crystals on the side are eliminated)
The maximum of the shower should be well contained in the fiducial volume
The length of the shower should be at least 40 cm (~21 X0)
Efficiency of these cuts~ 36%
Effective geometrical factor ~
(0.78*0.78*p)*5*e m2 sr= 9.55*e m2 sr
Gfeff~3.4 m2sr (including the efficiency)
calorimeter

## Slide 45
Electron #1

## Slide 46
Electron #1
cm
cm
Longitudinal profile
Signal
Integral Signal

## Slide 47
( Measured Energy – Real Energy ) / Real Energy
Electrons 100 – 1000 GeV
Energy resolution
Non gaussian tails due to leakages and to the carbon fiber material
RMS~2%

## Slide 48
( Measured Energy – Real Energy ) / Real Energy
Electrons 100 – 1000 GeV
Crystals only
Crystals + Photodiodes
1.7% difference

## Slide 49: Protons
Very simple geometrical cuts:
A good reconstruction of the shower axis
At least 50 crystals with >25 MIP signal
Energy is reconstructed by using the shower length measured in the calorimeter, since leakage are important (1.8 lI for perpendicular incidence)
calorimeter

## Slide 50
Proton #1

## Slide 51
Proton #1
cm
cm
Longitudinal profile
Signal
Integral Signal
Shower starting point is identified with ~1 cm resolution

## Slide 52
Shower Length (cm)
Signal / Energy
Proton 100 – 1000 GeV
Shower length can be used to reconstruct the correct energy
Red points: profile histogram
Fitted with exponential functions
To get the correct energy measurement

## Slide 53: Proton energy resolution
100 – 1000 GeV
1 TeV
10 TeV
32%
35%
39%
100 TeV
40%
( Measured Energy – Real Energy ) / Real Energy

## Slide 54: Efficiencies and Geometrical factors
GF(1 face) = 0.78*0.78*p m2 sr= 1.91 m2 sr
GF(5 faces)= 1.91*5 m2 sr = 9.55 m2 sr
Energy | e | Energy resolution | Gfeff (m2sr)
100-1000 GeV | 35% | 32% | 3.3
1 TeV | 41% | 34% | 3.9
10 TeV | 47% | 38% | 4.5
Selection cuts can be tuned to optimize the parameters
Roughly speaking: GF>3 m2sr with good energy resolution!!!!

## Slide 55: Some caveats….
Please note:
  The theoretical previsions for the knee region are really very much spread out!
  Pre-PAMELA-ATIC-CREAM scenarium: simple single power low up tp the knee region
  Post-PAMELA_ATIC_CREAM scenarium: the models have to exaplain the change in slope around 200 GV/c, and the different slopes btw protons and helium
  Differents sources, different injectiuon spectra, closeby sources,,non standard propagation scenarium….
Many works have been published in the last few years:
  Thoudam and Horandel
  Zatsepin, Panov, Sokolskaya.
  Bernard, Delahaye, Keum, Liu, Salati, Taillet
  Yuan, Zhang, Bi
  Tomassetti
  Blasi, Amato, Donato, Serpico
As a results, the expected spectrum around knee is unclear, and probably higher than the one expected up to few years ago
Possible structures may arise?
Direct measurementes are really essential!
With the propsed calorimeter, we could measure well above the knee
I can give you references if you are interested

## Slide 56: A spot on the pre-prototype test beam (m beam)
PD Only
PD Only
PD Only
PD Only

## Slide 57: A spot on the pre-prototype test beam (m- beam)
PD Only
PD Only
PD Only
PD Only

## Slide 58: A spot on the pre-prototype test beam (e- beam)
PD Only
PD Only
PD Only
PD Only

## Slide 59: Energy resolution
12.8 GV
Starting-layer ==2
Z=2
Z=1
82% (RMS)
39% (RMS)

## Slide 60: Energy resolution
12.8 GV
Starting-layer ==2
Z=2
Z=1
60% (fit)
34% (fit)